Deeper Insights
Unveiling Dopant Profiles with GIXRD
Mark Smith
Advisor: Brother Oliphant
Brigham Young University-Idaho

---
Definitions
- Dope
  - Adding a substance to a material to change certain characteristics about that material
- Dopant
  - Substance doing the doping

---
Definitions
- X-Ray Diffraction (XRD)
  - Broad category of techniques that shine x-rays at a sample to determine a variety of characteristics such as composition
  - There are powder and single crystal diffraction methods
- Grazing Incidence X-Ray Diffraction (GIXRD)
  - Specific type of XRD technique that uses single crystal XRD in order to have the x-rays only probe near the surface of the sample
  - This leaves the sample intact, preserving the layers

---
Definitions
- Crystalline
  - Type of material structure in which the atoms arrange themselves in a regular infinity repeatable pattern
- Amorphous
  - Type of material structure in which the atoms do not form an infinite repeatable pattern
- Crystalline Peak
  - Pattern Produced by crystalline parts of a material under XRD
- Amorphous Hump
  - Pattern produced by amorphous parts of a material under XRD

---
Background (Solids)
Two types of generalized solids
Amorphous (left)
Crystalline (right)

---
Background (Doping)
In this work samples of silicon that were doped with phosphorous were used. These were provided by the semiconductor team from their earlier doping trials.
Insert picture of samples

---
Background (Atomic Planes)

---
Background (Samples)
Two types of generalized solids
Amorphous (left)
Crystalline (right)

---
Background (XRD/GIXRD)
X-Ray Diffraction utilizes x-rays of Cu Kα wavelength (1.54Å)
Uses Bragg’s law:
2dsinθ=nλ
Diminishes according to:
I(y)=I0e−α y

---
Background (Single Crystal XRD)

---
Methods (Method 1)
Takes the highest value from the amorphous hump, and the highest value from the crystalline peak to find the ratio
Omega	Amorphous Range	Crystalline Range
6	13-33	60-63
5	12-31	59-61
3	14-35	36-38
m=\frac{I_a}{I_a+I_c}

---
Methods (Methods 2&3)
Curve Fit
Fits standard Gaussian function
Amorphous is yellow
Crystalline is green
Summation
Numerical integration on the regions

---
Analysis

---
Analysis

---
Conclusion
- Samples of dopant silicon with phosphorous were analyzed
- GIXRD was used to probe doped samples with x-rays to provide a diffractogram
- Three methods were used to analyze composition of doped samples using intensity, curve fitting, and summation
- The methods come close in their agreement for depth of how far the dopant penetrated into the sample

---
Future Work

---
References