Deeper Insights
Unveiling Dopant Profiles with GIXRD
Mark Smith
Advisor: Brother Oliphant
Brigham Young University-Idaho

---
Definitions
- Dope
  - Adding a substance to a material to change certain characteristics about that material
- Dopant
  - Substance doing the doping

---
Definitions
- X-Ray Diffraction (XRD)
  - Broad category of techniques that shine x-rays at a sample to determine a variety of characteristics such as composition
  - There are powder and single crystal diffraction methods
- Grazing Incidence X-Ray Diffraction (GIXRD)
  - Specific type of XRD technique that uses single crystal XRD in order to have the x-rays only probe near the surface of the sample
  - This leaves the sample intact, preserving the layers

---
Definitions
- Crystalline
  - Type of material structure in which the atoms arrange themselves in a regular infinity repeatable pattern
- Amorphous
  - Type of material structure in which the atoms do not form an infinite repeatable pattern
- Crystalline Peak
  - Pattern Produced by crystalline parts of a material under XRD
- Amorphous Hump
  - Pattern produced by amorphous parts of a material under XRD

---
Background (Solids)
Two types of generalized solids
Amorphous (left)
Crystalline (right)

---
Background (Atomic Planes)
When x-rays interact with bulk samples, all atomic planes participate in the resulting diffraction.

---
Background (Doping)
In this work samples of silicon that were doped with phosphorous were used. These were provided by the semiconductor team from their earlier doping trials.

---
Background (Samples)
The doped samples have an atomic similar to what is shown here.

---
Background (XRD/GIXRD)
X-Ray Diffraction utilizes x-rays of Cu Kα wavelength (1.54Å)
Uses Bragg’s law:
2dsinθ=nλ
Diminishes according to:
I(y)=I0e−α y

---
Background (Single Crystal XRD)
- Single crystal XRD leaves the sample intact, with the plane of atoms aligned in their preferred orientation
- This means alignment is everything

---
Methods (Method 1)
Takes the highest value from the amorphous hump, and the highest value from the crystalline peak to find the ratio
Omega	Amorphous Range	Crystalline Range
6	13-33	60-63
5	12-31	59-61
3	14-35	36-38
m=\frac{I_a}{I_a+I_c}

---
Methods (Methods 2&3)
Curve Fit
Fits standard Gaussian function
Amorphous is yellow
Crystalline is green
Summation
Numerical integration on the regions

---
Analysis

---
Conclusion
- Samples of dopant silicon with phosphorous were analyzed
- GIXRD was used to probe doped samples with x-rays to provide a diffractogram
- Three methods were used to analyze composition of doped samples using intensity, curve fitting, and summation
- The methods come close in their agreement for depth of how far the dopant penetrated into the sample

---
Future Work
- The Surface Physics group is building a deposition machine that will have an oscillator in their to determine layer thickness to compare to
- Nonuniform layers

---
References